## Slide 1: Proposal for improved passive building ventilation

## Slide 2: Benefits
Low cost
  (hundreds not thousands)
Fast implementation
  (days not weeks)
Improve occupant experience
  (passive cooling early mornings/late evenings)
Improve security
  (eliminate propped open doors)
Opportunity for artistic expression
  (combination of flat bar elements and paint can provide drastic impact)

## Slide 3: proposal
Install security “screen doors” on the North and South entrance inner vestibule door frames. These openings had their wood frame doors removed at some point in history, but remain viable for reuse.
Proposed doors would consist of the following:
  Box tube steel frame
  Flatted expanded metal infill
  Vertical panic bar hardware (meet emergency egress requirements)
  Automatic door closers (keeps building secure)
  Potential enhancements:
    Incorporate artistic elements (Wichita flag/banner?)
    Insect screens easily added

## Slide 4: Materials (four total doors N/S hallway)
80 feet 1 ½ x 3 x .083 box tubing ($400)
4 sheets 4 x 8 x .156 flattened expanded metal ($480)
4 sets vertical panic bar door hardware ($340-876)
4 sets door closers ($202-560)
4 sets commercial door hinges ($55-110)
8 sets of door hold open hardware ($104-120)
        TOTAL $1,581-2,546*
        *Given the low usage these doors should receive recommend lighter grade hardware